## Slide 1: 2024 Solar Eclipse Traffic Management Plan
ARDOT Transportation Research Conference
May 22, 2024
Nicci Tiner, PE, PTOE

## Slide 2: Introduction
On April 8, 2024, the Moon passed between the Sun and the Earth, creating a 117.9-mile-wide shadow.
In preparation for this event, Garver prepared a Traffic Management Plan for ARDOT.

## Slide 3
Data Compilation & Traffic Forecasting

## Slide 4: Data Compilation
Information from the Arkansas State Parks
Booking data for hotels, campgrounds, and RV parks
After-Action Plans from the 2017 Eclipse
Miscellaneous websites

## Slide 5: Traffic Forecasting
Up to 1.5 million visitors expected to visit and 500,000 Arkansans travelling also.
Assumed 2.86 passengers per vehicle
Reviewed the 2017 Eclipse to develop travel patterns
  30% arrive day of the event
  80% leave immediately afterwards

## Slide 6: Travel Demand Modelling
Alliance Transportation Group (ATG) partnered with us on this project.
Using the available information, ATG modified the Statewide Travel Demand Model (TDM).
Based on the TDM results, the Team (ARDOT, ATG, and Garver) identified hot spots and corridors needing mitigation.

## Slide 7: Travel Demand Model Results
Extreme (Purple) = bottleneck points
Very high (Red) = well above capacity
High (Orange) = above capacity
Significant (Blue) = approach or modestly exceed capacity

## Slide 8
Traffic Demand Reduction Strategies

## Slide 9: Traffic Demand Reduction Strategies
Stay a While
  Festivals and activities across the state promoted tourist to stay afterwards

## Slide 10: Traffic Demand Reduction Strategies
Stay a While
  Festivals and activities across the state promoted tourist to stay afterwards
School Closings
  Over 100 school districts were closed

## Slide 11: Traffic Demand Reduction Strategies
Stay a While
  Festivals and activities across the state promoted tourist to stay afterwards
School Closings
  Over 100 school districts were closed
Work from Home
  Many employees worked from home

## Slide 12: Traffic Demand Reduction Strategies
Oversized Loads
  ARDOT limited permits for oversized loads the day of the event
Truck Holiday
  Truckers were encouraged to adjust travel schedules
  Data shows that truck traffic was down approximately 50% on April 8, 2024
32% Trucks (Typ.)

## Slide 13
Traffic Flow Enhancements

## Slide 14: Reduce Construction Activity
Reduce construction activity and in particular lane closures
Special provision prohibited main lane closures from Friday, April 5 through Tuesday, April 9
Unfortunately, the lane closure on the I-55 River Bridge in Memphis was under TDOT jurisdiction. The EB lane closure was still in place.

## Slide 15: Response Positioning
Performed a systemwide review of bottleneck points
Prioritized routes
Created a dashboard
ARDOT District employees had editing access to this dashboard

## Slide 16: Response Positioning
Strategically station law enforcement, ARDOT field crews, and towing services at intersections where colored routes cross, and intersections leading to state parks

## Slide 17: Response Positioning
Located at various locations such as interchanges, signalized intersections on the purple, red, and some orange routes

## Slide 18: Spot Mitigation I-55 at I-555
Prepared for potential lane closure on SB I-55 to allow SB I-555 entrance ramp to become free flowing
Outside lane becomes an exit only lane

## Slide 19: Spot Mitigation I-40 at I-49
Advance signing prior to the Alma exit
Drone coverage
Tow trucks
ARDOT and police personel

## Slide 20: Spot Mitigation I-30 at Hwy 70
Prepared for potential lane closure on NB I-30 to allow Hwy 70 entrance ramp to become free flowing.
Outside lane becomes an exit only lane

## Slide 21
Eclipse Day – April 8, 2024

## Slide 22: Traffic Management Center
TMC collected live information from:
  Cameras
  On-the-ground personnel
  Online sources
TMC disseminated information:
  Flagging crews
  Enforcement personnel
  Emergency responders

## Slide 23: Hot Spots Statewide
  Post eclipse traffic at approximately 3:15 PM

## Slide 24: Hot Spots I-555 prior to I-55
  Post eclipse traffic at approximately 3:30 PM
  Normal day traffic at this location is 14,000 vpd
  April 8, 2024, traffic was 28,500 vpd (more than double)

## Slide 25: Hot Spots I-555 at I-55
  Post eclipse traffic at approximately 3:25 PM
  Normal day traffic south of the entrance ramp is 31,000 vpd
  April 8, 2024, traffic was 40,500 vpd (30% increase)

## Slide 26: Hot Spots I-40 at I-55
  Congestion began not long after the eclipse was over
  Primarily traffic coming from Jonesboro via I-55

## Slide 27: Hot Spots I-40 at I-55
  The congestion continued through the evening
  The images are from around 8:10 PM on April 8, 2024

## Slide 28: Hot Spots I-40 near Russellville
  Post eclipse traffic at approximately 2:20 PM

## Slide 29: Hot Spots I-40 near Russellville
  Post eclipse traffic at approximately 3:20 PM

## Slide 30: Hot Spots I-40 at I-440
  Post eclipse traffic

## Slide 31: Hot Spots I-40 at I-440
  Post eclipse traffic at approximately 3:25 PM

## Slide 32: Not So Hot Spot Hwy 70 at I-30
  Post Eclipse Traffic
  Normal day traffic on I-30 between Reynold’s Road and I-430 is 115,000 vpd and 19,000 vpd on Hwy 70
  April 8, 2024, traffic at that location was 76,000 vpd (35% decrease) on I-30 and 15,000 vpd (15% decrease) on Hwy 70

## Slide 33: Not So Hot Spot Hwy 70 at I-30
  Post eclipse traffic at approximately 3:00 PM

## Slide 34
After-Action Plan

## Slide 35: After-Action Plan
Currently working on the After-Action Plan

## Slide 36: After-Action Plan
Data collection during the Eclipse
  20 ATR Stations Counts
  22 Miovision Counts
  46 Tube Counts

## Slide 37: After-Action Plan
Tabulated the traffic data taken during the eclipse

## Slide 38: After-Action Plan
Plotted segments where data was collected

## Slide 39
Questions